## Slide 1: Arduino Step by Step Getting Serious
Name: JOYDIP DUTTA
Branch: Electronics And Communication Engineering
Semester: VII
Roll Number: 17EREEC006

## Slide 2: Certificate of Completion of the Course

## Slide 4: Course Overview
Getting Familiar with Development Boards
Software Installations
SENSORS, ACTUATORS, AND DISPLAYS
Demonstration Video of some Projects.

## Slide 5: Getting Familier with Development Board
Arduino UNO
NodeMCU ( ESP12E )
ESP32-WROOM-32D
SECTION-1

## Slide 6: GETTING FAMILIER WITH DEVELOPMENT BOARD
Open-source hardware platform
Affordable hardware
Easy to set-up for basic applications
Well established community support
Easily expandable functionality with on-top shields and GPIO available on-board
Arduino Uno, Arduino YUN (with Wi-Fi), Arduino MKR family (with Wi-Fi, BLE, LoRa, SigFox and Narrowband IoT)
INTRODUCTION TO ARDUINO UNO
SECTION-1A

## Slide 7: OVERVIEW OF ARDUINO UNO
SECTION-1A

## Slide 8: PIN CONFIGURATIONS OF ARDUINO UNO
SECTION-1A

## Slide 9: MIND OF THE ARDUINO ( ATMEGA328P)
SECTION-1A

## Slide 10: GETTING FAMILIER WITH DEVELOPMENT BOARD
Also known as ESP8266 development board.
Affordable hardware for IoT Projects.
Easy to set-up for basic applications
Well established community support
NodeMCU is an open-source LUA based firmware developed for the ESP8266 WiFi chip.
Espressif System (A Shanghai-based Semiconductor Company) has released this adorable, bite-sized WiFi-enabled microcontroller - ESP8266 chip.
INTRODUCTION TO NodeMCU
SECTION-1B

## Slide 11: OVERVIEW OF NODEMCU
ESP-12E WiFi Module
This ESP-12E module containing an ESP8266 chip having Tensilica Xtensa® 32-bit LX106 RISC microprocessor which operates at 80 to 160 MHz adjustable clock frequency and supports RTOS.
There’s also 128 KB RAM and 4MB of Flash Memory is available which is enough to cope with large strings that make up web pages, JSON/XML data, and everything we use in IoT devices nowadays.
The most versatile feature of NodeMCU is that it can set up a network of its own which allows the other devices to connect directly to it. This is possible because ESP8266 integrates 802.11b/g/n HT40 Wi-Fi transceiver.
This module has 2.4 GHz Antenna which is enough to give us a proper range for our projects.
SECTION-1B

## Slide 12: OVERVIEW OF NODEMCU CONTINUES
Power Requirements
Operating Voltage: 2.5V to 3.6V
On-board regulator: 3.3V 600mA regulator
Operating Current: 80mA
Current during Sleep Mode: 20 µA
SECTION-1B
Peripherals & Input/Output
Total GPIO pins: 17
ADC channel: A 10-bit ADC channel
UART interface: UART interface is used to load code serially.
PWM outputs: PWM pins for dimming LEDs or controlling motors.
SPI & I2C: SPI and I2C interface to hook up all sorts of sensors and peripherals.
I2S Interface: I2S interface if you want to add sound to any project.
Multiplexing Feature: A single GPIO pin can act as PWM/UART/SPI.

## Slide 13: OVERVIEW OF NODEMCU CONTINUES
On Board Switches & LEDs
RST Button: Reset the ESP8266 chip
FLASH Button: Download new programs
Blue LED: Work as an Indicator. (User Programmable)
SECTION-1B
Serial Communication
CP2102 USB-to-UART converter: It is a bridge converter which converts USB signal to Serial. This allows our computer to program and communicate with the ESP8266 chip.
Communication Speed: 4.5Mbps.

## Slide 14: PIN DESCRIPTION OF NODEMCU BOARD
SECTION-1B
Pins (according to functionality) | Availability | Description
Power Pins | One Vin pin, three 3.3V Pins(Vout), and Five ground Pins are available. | Vin Pin: Used to provide power supply to the board directly. 3.3V Pin: Used to supply power to external components.
I2C Pins | D1 and D2 pin are available as an SCL and SDA pin respectively. | D1 and D2 are used to hook up all sorts of I2C Sensors.
GPIO Pins | There are 17 pins are available as GPIO. | These pins can be assigned to various functions programmatically.
ADC Channel | VDD3P3 pin and TOUT pin. | Used as an ADC pin but cannot be implemented at the same time.
UART Pins | UART0 ( TXD0, RXD0, RST0, and CTS0 Pins ) UART1 ( TXD1 Pin) | UART0: can be used for communication and it supports fluid control. UART1: It features only the data transmit signal.

## Slide 15: PIN DESCRIPTION OF NODEMCU BOARD CONTINUES
SECTION-1B
Pins (according to functionality) | Availability | Description
SPI Pins | SPI and HSPI Pins. | Supports 4 timing modes of the SPI format transfer.
PWM Pins | Four Channels of PWM. | PWM can be implemented programmatically. The frequency range is adjustable from 1000 μs to 10000 μs, i.e., between 100Hz and 1 kHz.
Control Pins | Enable Pin(EN), Reset Pin(RST) & WAKE pin. | EN pin: Control the ESP8266 chip by set it as a HIGH and LOW. RST pin: Used to Reset the ESP8266 chip. WAKE pin: Used to wake the chip from a deep-sleep mode.
SPI Pins | SPI and HSPI Pins. | Supports 4 timing modes of the SPI format transfer.

## Slide 16: PIN DESCRIPTION OF NODEMCU BOARD CONTINUES
SECTION-1B
https://cybotians.com
https://cybotians.com
https://cybotians.com

## Slide 17: GETTING FAMILIER WITH DEVELOPMENT BOARD
ESP32 is a series of low cost, low power system on chip microcontrollers with integrated Wi-Fi & dual-mode Bluetooth.
Easy to set-up for basic applications
Well established community support
ESP32 is created and developed by Espressif Systems, a Shanghai-based Chinese company
INTRODUCTION TO ESP32
SECTION-1C

## Slide 18: OVERVIEW OF ESP32
SECTION-1C

## Slide 19: OVERVIEW OF ESP32
SECTION-1C

## Slide 20: OVERVIEW OF ESP32
SECTION-1C

## Slide 21: OVERVIEW OF ESP32
SECTION-1C

## Slide 22: OVERVIEW OF ESP32
SECTION-1C

## Slide 23: PIN DESCRIPTION OF ESP32-WROOM-32
SECTION-1C
https://cybotians.com
https://cybotians.com
https://cybotians.com

## Slide 24: SOFTWARE INSTALLATIONS
Arduino IDE
SECTION-2

## Slide 25: SOFTWARE INSTALLATIONS CONTINUES
SECTION-2A

## Slide 26: SOFTWARE INSTALLATIONS CONTINUES
http://arduino.esp8266.com/stable/package_esp8266com_index.json ,
https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json
SECTION-2A

## Slide 27: SENSORS, ACTUATORS, AND DISPLAYS
Sensors
A sensor detects (senses) changes in the ambient conditions or the state of another device or a system, and forwards or processes this information in a certain manner. They perform some input functions by sensing or feeling the physical changes in characteristics of a system in response to stimuli. For example, heat is converted to electrical signals in a temperature sensor, or atmospheric pressure is converted to electrical signals in a barometer.

## Slide 28: SENSORS, ACTUATORS, AND DISPLAYS
Actuators
An actuator is a component of a machine or system that moves or controls the mechanism or the system. An actuator is a mechanism by which a control system acts upon an environment An actuator requires a control signal and a source of energy. Upon receiving a control signal, the actuator responds by converting the energy into mechanical motion. The control system can be simple (a fixed mechanical or electronic system), software‐based (e.g. a printer driver, robot control system), a human, or any other input.

## Slide 29: SENSORS, ACTUATORS, AND DISPLAYS
Displays
A display device is an output device for the presentation of information in a visual or tactile form (the latter used for example in tactile electronic displays for blind people). When the input information that is supplied has an electrical signal the display is called an electronic display. Here, I have discussed the interfacing of some common display boards with Arduino Uno.

## Slide 30: Before starting the interfacing, Let’s See Where to find the codes for this topic
https://github.com/joydipdutta001/ArduinoStepByStep

## Slide 31: Temperature and Humidity Sensor ( DHT22 )
Technical Specifications:
Operating Voltage: 3.5V to 5.5V
Operating current: 0.3mA (measuring) 60uA (standby)
Output: Serial data
Temperature Range: -40°C to 80°C
Humidity Range: 0% to 100%
Resolution: Temperature and Humidity both are 16-bit
Accuracy: ±0.5°C and ±1%

## Slide 32: How to Use DHT22 Sensor module:
Pin | Wiring to Arduino Uno
1st pin- VCC | 5V
2nd pin- DataOUT | Digital pin 2
3rd pin | Not need to connect
4th pin- GND | GND
Circuit Diagram ( Schematics ):

## Slide 33: Environmental Sensor ( BMP180 )
Technical Specifications:
Operating voltage of BMP180: 1.3V – 3.6V
An input voltage of BMP180MODULE: 3.3V to 5.5V
Peak current: 1000uA
Consumes 0.1uA standby
Maximum voltage at SDA , SCL : VCC + 0.3V
Operating temperature: -40ºC to +80ºC

## Slide 34: How to Use MP180 Module?
Pin | Wiring to Arduino Uno
Vin | 5V
GND | GND
SCL | A5
SDA | A4
Circuit Diagram ( Schematics ):

## Slide 35: Motion Sensor and Accelerometer ( MPU6050 )
Technical Specifications:
MEMS 3-axis accelerometer and 3-axis gyroscope values combined
Power Supply: 3-5V
Communication: I2C protocol
Built-in 16-bit ADC provides high accuracy
Built-in DMP provides high computational power
In-built temperature sensor

## Slide 36: How to Use MPU6050 Module?
Circuit Diagram ( Schematics ):
Pin | Wiring to Arduino Uno
Vin | 5V
GND | GND
SCL | A5
SDA | A4
INT | 2

## Slide 37: Ultrasonic Distance Sensor ( HC-SR04 )
Technical Specifications:
Operating voltage: +5V
Theoretical Measuring Distance: 2cm to 450cm
Practical Measuring Distance: 2cm to 80cm
Accuracy: 3mm
Measuring angle covered: <15°
Operating Current: <15mA
Operating Frequency: 40Hz

## Slide 38: How to Use HC-SR04 Module?
Circuit Diagram ( Schematics ):
Pin | Wiring to Arduino Uno
VCC | 5V
Trig | 9
Echo | 12
GND | GND

## Slide 39: Passive Infrared Sensor ( PIR )
Technical Specifications:
Wide range on input voltage varying from 4.V to 12V (+5V recommended)
The output voltage is High/Low (3.3V TTL)
Can distinguish between object movement and human movement
Has to operate modes - Repeatable(H) and Non- Repeatable(H)
It can cover a distance of about 120° and 7 meters
Low power consumption of 65mA
Operating temperature from -20° to +80° Celsius

## Slide 40: How to Use PIR Module?
Circuit Diagram ( Schematics ):
Pin | Wiring to Arduino Uno
VCC | 5V
OUT | 2
GND | GND

## Slide 41: Color Sensor Module ( TCS320 )
Technical Specifications
Input voltage: (2.7V to 5.5V)
Interface: Digital TTL
High-resolution conversion of light intensity to frequency
Programmable color and full-scale output frequency
No need for ADC(Can be directly connected to the digital pins of the microcontroller)
Power down feature
Working temperature: -40oC to 85oC
Size: 28.4x28.4mm(1.12x1.12")

## Slide 42: How to Use TCS3200 Color Sensor Module?
Circuit Diagram ( Schematics ):
Pin | Wiring to Arduino Uno
S0 | Digital Pin 4
S1 | Digital Pin 5
VCC | 5V
S3 | Digital Pin 6
S4 | Digital Pin 7
OUT | Digital Pin 8

## Slide 43: Gas Sensor Module ( MQ135 )
Technical Specifications
Wide detecting scope
Fast response and High sensitivity
Stable and long life
Operating Voltage is +5V
Detect/Measure NH3, NOx, alcohol, Benzene, smoke, CO2, etc.
Analog output voltage: 0V to 5V
Digital output voltage: 0V or 5V (TTL Logic)
Preheat duration 20 seconds
Can be used as a digital or analog sensor

## Slide 44: How to Use MQ135 Gas Sensor Module?
Circuit Diagram ( Schematics ):
Pin | Wiring to Arduino Uno
A0 | Analog pin A0
VCC | 5V
GND | GND

## Slide 45: Displays And Actuators
Liquid Crystal Display (LCD) Module ( Size: 2x16 )
Seven Segment Displays (Single Digit)
An 8x8 LED matrix display
DC Motors And Arduino Uno
Servo Motors And Arduino Uno
Displays:
Actuators:

## Slide 46: Project: Wireless Display Board with Temperature, Humidity and Smoke Measurement
Let’s See Some Demo

## Slide 47: Project: Room Automation With Android App And Two way Switching
Let’s See Some Demo Continues

## Slide 48: THANK YOU